Adjusting accuracy by applying changes on model penalty values

In order to test out examples on the HMM we have created we use the next built-in HTK command tool:
HVite -A -D -T 1 -H hmm9/macros -H hmm9/hmmdefs -C config -S test.scp -l '*' -i ../test/mfcc/recout_penalty-X.mlf -w wdnet -p -X.0 -s 5.0 ../lexicon/voxforge_lexiconV2 ../auto/tiedlist

By setting penalty value to 0 we get the following result: WORD: %Corr=85.37, Acc=-263.76 [H=245, D=1, S=41, I=1002, N=287]
As we can see taccuracy is below zero which is caused the many insertions we have let to system to apply. In this moments we need deletion error to be equal to insertion error. So we set the penalty with a negative value until we achieve equality between D and I.

P= -20.0
SENT: %Correct=48.95 [H=140, S=146, N=286]
WORD: %Corr=95.12, Acc=-67.94 [H=273, D=1, S=13, I=468, N=287]

P=-50
SENT: %Correct=63.99 [H=183, S=103, N=286]
WORD: %Corr=94.43, Acc=11.15 [H=271, D=1, S=15, I=239, N=287]

P=-100.0
SENT: %Correct=74.48 [H=213, S=73, N=286]
WORD: %Corr=94.77, Acc=44.25 [H=272, D=1, S=14, I=145, N=287]

P=-200.0
SENT: %Correct=84.27 [H=241, S=45, N=286]
WORD: %Corr=94.43, Acc=73.87 [H=271, D=1, S=15, I=59, N=287]

P=-400.0
SENT: %Correct=92.31 [H=264, S=22, N=286]
WORD: %Corr=94.43, Acc=91.29 [H=271, D=1, S=15, I=9, N=287]

P=-600.0
SENT: %Correct=93.71 [H=268, S=18, N=286]
WORD: %Corr=94.43, Acc=93.73 [H=271, D=1, S=15, I=2, N=287]

P=-800.0
SENT: %Correct=94.06 [H=269, S=17, N=286]
WORD: %Corr=94.43, Acc=94.08 [H=271, D=1, S=15, I=1, N=287]